Holy Family STEM
September 23, 2016

---
Hypothesis
- What was your hypothesis for the beam?
- How where you going to test?

---
E for Engineering
- Engineer’s create hypothesis constantly
- Test using
  - Models
  - Simulation
- Generally not possible to build full scale

---
M is for Math
- Definitions
  - Constant: A value that does not change
  - Variable:
    - A value that may change
    - An abstract to simplify a more complex concept
- Basic Beam equations: A model

---
Beam Calculations
%delta = {FL^3} over {48EI}
For a simple supported beam, the deflection is given by:
Where:
F: The force applied
L: The length of the beam
E: Modulus of Elasticity of the material
I: Moment of Inertia
The moment of inertia depends on the shape.
For a round cross section:
Where d is the diameter of the cross section
For a rectangular cross section:
Where w is the width and h is the height
I = {%pi d^4} over {64}
I = {w h^3} over {12}

---
Demo

---
Next week: Pulleys for mechanical advantage

---
Today’s build
- Build a ramp for a ball to roll down
- Use what you just learned about the shape of the beams
- The ball must strike another ball and move it 6 inches